## Slide 1: Τεχνολογία Προηγμένων Ψηφιακών Κυκλωμάτων & Συστημάτων 2005
Εργασία 2η
Πρόβλημα 6-23 Rabey

## Slide 2: Πρόβλημα 6-23
Figure 6.16 shows a dynamic CMOS circuit in domino logic.
In determining source and drain areas and perimeters, you may use the following approximations AD=AS=W*0.625 μm and PD=PS=W+1.25 μm.
Assume 0.1ns rise/fall times for all inputs, including the clock.
Furthermore, you may assume that all the inputs and their complements are available, and that all inputs change during the precharge phase of the clock cycle.

## Slide 3: Figure 6.16

## Slide 4: Question A
What Boolean functions are implemented at outputs F and G?
If A and B are interpreted as two-bit binary words, A = A1A0 and B = B1B0 , then what interpretation can be applied to output G?

## Slide 5: Solution A1
O1 = (A0 B0 + A0 B0 )
F = (A0 B0 + A0 B0 )
O2 = F (A1 B1 + A1 B1 )
G = F (A1 B1 + A1 B1 )

## Slide 6: Solution A2
Αν θεωρήσουμε ως είσοδο τα Α = A1A0 , Β = B1B0
τότε η έξοδος G = 1 αν Α=Β.
Αν Α=Β => A1=B1 κ’ A0=B0
F = (A0 B0 + A0 B0 ) = (A0 + A0 ) = 1
G = F (A1 B1 + A1 B1 ) = 1(A1 + A1) = 1
Μια συσκευή σύγκρισης των εισόδων Α , Β.

## Slide 7: Question Β
Which gate (1 or 2) has the highest potential for harmful charge sharing and why ?
What sequence of inputs (spanning two clock cycles) results in the worst-case charge-sharing scenario ?

## Slide 8: Solution B1
Η πύλη 2 «υποφέρει»
περισσότερο σε μια υπερφόρτωση
διότι το φορτίο μοιράζεται σε
μεγαλύτερη χωρητικότητα από ότι
στην πύλη 1.
Στην πύλη 2 τα τρανζίστορ
έχουν διπλάσιο W από ότι στην
πύλη 1. Οπότε η παρασιτική
χωρητικότητα της πύλης 2 θα
είναι περίπου διπλάσια από
ότι στην πύλη 1.

## Slide 9: Solution B1
W = 1
Για κάθε τρανζίστορ:
AD=AS=W*0.625 = 0.625μm , PD=PS=W+1.25 = 2.25μm
Με παρασιτική χωρητικότητα CL1
W = 2
Για κάθε τρανζίστορ:
AD=AS=W*0.625 = 1.25μm , PD=PS=W+1.25 = 3.25μm
CL2 = 2 CL1 ( περίπου )

## Slide 10: Solution B2
1st cycle
A0 ≠ B0 A1 = B1
outGate1=high , F= low
outGate2=high
2nd cycle
A0 =B0 A1 ≠ B1
outGate1=low , F= high
outGate2  low

## Slide 11: Solution B2
  Για παράδειγμα αν έχω
  A1=B1= VDD στον 1ο
  κύκλο και μια μετάβαση σε
  A1=VDD , B1=0 στον 2ο
  κύκλο θα προκαλέσει το
  μοίρασμα του φορτίου στην
  έξοδο της πύλης 2 στις
  παρασιτικές χωρητικότητες
  του drain των A1 , A1 , B1
  τρανζίστορ.

## Slide 12: Spice

## Slide 13
Φοιτητής: Πολυχρονόπουλος Ανδρέας
ΑΜ: 4700